METROPOLITAN JUDGING FORM

International Meet –Metropolitan Owners Club of North America

REVISED 4/25/06 APPROVED FOR 2009  INTERNATIONAL

| CAR # | CONCOUR CLASS |
| --- | --- |
| FEATURE | MAX DED | DED | COMMENTS |
| EXTERIOR |
| Beading & Seams Deduct max of 1 point total, at these areas; Rear fender beading. Front fender near windshield. Headlight to grille (seam shows prior to 1957). Under headlights. Under taillights. Each end of rocker panels. | 5 |  |  |
| Body | Door (dents & scratches) | 5 ea |  |  |
|  | Fender F&R (dents & scratches) | 5 ea |  |  |
|  | Hood (dents & scratches) No deduction for Flying Lady hood ornament Wrong hood-No scoop beg. E-21008 | 4 (10)* |  |  |
|  | Top – Metal (dents & scratches) | 4 |  |  |
|  | Trunk External opening Beg.E59048, check for black, lid liner | 4 |  |  |
|  | Improper trunk no lid before E-59048 | (10)* |  |  |
|  | Side molding -Beg. E21008 Dings/scratches- 1 point per piece | 6 |  |  |
|  | Side moldings before E21008 | (6)* |  |  |
|  | Color Colors reversed, or Non Met colors Wrong color from plate/unreasonable match | (30)* 10 |  |  |
|  | Paint lines/break check insides of doors, hood, and under taillights | 3 |  |  |
|  | Improper body (convertible from coupe, check doors for extra dovetail and under-car support brackets) | (40)* |  |  |
|  | Door handles (plating/paper gaskets, correct handles) square locks beg E48848 | 3 ea |  |  |
| Lights Headlamp (rubber/chrome/glass/ Correct bezels) bulbs should match | 4 ea |  |  |
|  | Parking (rubber/chrome/glass) | 3 ea |  |  |
|  | Tail (Lucas 523)/ bezel (condition) | 2 ea |  |  |
| BONUS POINTS | GE in circle, sealed beams | 3 ea |  |  |
| External Mirror (plating/condition/glass) | 3 |  |  |
| * NUMBERS IN PARENTHESES ARE AUTOMATIC DEDUCTIONS page 1 |
| METROPOLITAN JUDGING FORM |
| CAR# CONCOURS |
| EXTERIOR |
| FEATURE | MAX DED | DED | COMMENTS |
| Radiator – Grille condition/plating (Mesh type beg E21008) | 5 |  |  |
|  | Wrong grille | (10)* |  |  |
|  | Grille surrounds (beg E21008) condition | 4 |  |  |
|  | Ornament/medallion (Nash/Hudson, M only beg E28327) chrome/paint/scratches | 3 |  |  |
| Windshield (two piece molding beg E-79091, Except E79067, 71,75,76,78,80,81 (Rubber/stainless steel trim/glass) Wrong windshield trim | 3 (2)* |  |  |
| Bonus Triplex toughened logo on windshield glass | 2 |  |  |
| Windows/glass (rear to one piece beg. E45672) Vent windows before E-59048 | 5 (2)* |  |  |
| Windshield Wipers (plating, rubber, sit parallel to trim) | 4 |  |  |
| Wrong wiper arms (should have crook, not straight) | (2)* |  |  |
| Trunk/door/roof rail weather seals (trunk drain hoses must be black with wire clamps)(condition of aluminum end plates on doors) | 6 |  |  |
| Fender script (NKI)(Metropolitan beg E2869) | 2 |  |  |
| Fender script on both sides | (2)* |  |  |
| Trunk Gaskets handle/hinges (should be paper) | 5 |  |  |
| Bumpers & Guards (Plating condition, black rubber insulators, bumper spacers, bumper bolts) | 12 |  |  |
| Hub Caps (M only beg. E10007) (paint/plating) | 2 ea |  |  |
| Spare tire cover/cap (cap mist gray or white) (plain cap only beg. E21008)(cover is green w/black piping, beg. E21008 black w/white piping) | 6 |  |  |
| Total deductions _______ Judge_________________________________________________ * NUMBERS IN PARENTHESES ARE AUTOMATIC DEDUCTIONS page 2 |
| METROPOLITAN JUDGING FORM |
| Car# CONCOURS CLASS |
| FEATURE | MAX DED | DED | COMMENTS |
| CHASSIS |
| Undercarriage (body color or black undercoating) Check battery box here | 5 |  |  |
| Axles/ suspension/Shock Absorbers (painted black, Differential carrier natural aluminum) | 5 |  |  |
| Brakes/Master Cylinder (wheel cyl. Change beginning E29284, 5/8” master cylinder after E29283) | 2 |  |  |
|  | Disc Brakes | (4)* |  |  |
| Exhaust system/ Clamps/ Hangers (3-hole clamp on A-40 engines, split V clamp after) (3 hangers are used.) | 3 |  |  |
|  | Glass pack muffler | (3)* |  |  |
| Gas Tank/ Straps/ Grommets/ Filler Cap (cap body color, tank and straps, black) | 2 |  |  |
|  | Fiberglass gas tank | (2)* |  |  |
| Wheels (All 5) (Mist Grey), beg. E-21008 wheels painted body color) (check for correct wheels, ie. riveted, welded, valve stem size) | 2ea |  |  |
| Tires (5.20x13, 5.60x13 beg E21008) (all 5- tires same brand) Deduct for narrow white stripe | 2ea |  |  |
| Bonus | Goodyear bias ply 2-1/4” Whitewall | 1ea |  |  |
| Transmission/Drive Line/Leaf Springs & Clamps (hyd. clutch beg. E11001) (clutch slave cyl change to cast ears beg. E59048) | 2 |  |  |
| Tow Hooks missing/wrong color (front hook plates must match fan color, red or beginning approx E-65952 yellow) (rear tie downs are body color) | 4 |  |  |
| Overall cleanliness 4____________________________________ Total Deductions ______ Judge __________________________________________________ * NUMBERS IN PARENTHESES ARE AUTOMATIC DEDUCTIONS page 3 |
| METROPOLITAN JUDGING FORM |
| CAR# CONCOURS CLASS |
| FEATURE | MAX DED | DED | COMMENTS |
| INTERIOR |
| Dashboard/Molding (body color/ beginning E-21008 gloss black) (black around windshield beginning E-21008) | 4 |  |  |
|  | Wrong color | (3)* |  |  |
|  | Improper glove box (glove box door avail. Beg. E21008, standard beg. E44800) | (3)* |  |  |
| Owners manual (correct for car/condition) | 2 |  |  |
| Upholstery (condition) Rips or tears, scuff’s, open seams | 10 |  |  |
|  | Wrong pattern (doors, seats) Pattern of cloth to vinyl | (10)* |  |  |
|  | Wrong materials (non Met OEM or unreasonably close to original) | (10)* |  |  |
| Storm strip (condition) | 2 |  |  |
|  | Wrong color | (5)* |  |  |
| Black Rubber Floor Mat (condition) | 5 |  |  |
|  | Carpet instead of mat | (5)* |  |  |
| Headliner (hardtop only) (condition, water stains) | 3 |  |  |
| Sun visors (heat seamed beg. E21008) (hardware, brackets, material) | 3 ea |  |  |
| Door sills (condition & screws) Reproduction sills w/out complete rolled edge | 3ea (1)* |  |  |
| Ashtray (lid, base, and springs) (airflyte script ended E10007) | 2 |  |  |
| Rear view mirror (condition glass/hardware) | 2 |  |  |
| Instruments (condition/plating) (Speedometer; dial, Needle, Gasket) (High-beam indicator) (Fuel gage) (Turn signal indicator) | 5 |  |  |
| Radio knobs & pointer (condition) | 4 |  |  |
| Radio antenna (correct/condition) (Black phenolic base, gasket, stem and ball) | 2 |  |  |
| Cigar lighter (correct/condition) Knob, element & base | 2 |  |  |
| Switches/Knobs Headlight switch, pull to start knob, choke, heater, wiper, turn signal switch, horn button (Bulls-eye horn button only beg. E21008) | 7 |  |  |
| Handles & escutcheons condition and correctness (cream escutcheons, black beg. E21008) | 4 |  |  |
| Gear shift lever/knob (plating/condition) | 4 |  |  |
| Page 4 |
| METROPOLITAN JUDGING FORM |
| CAR# CONCOURS CLASS |
| FEATURE MAX DED COMMENTS DED |
| INTERIOR |
| Pedals (condition of rubber pads) | 3 |  |  |
| Added gauges (condition/correct vintage) | 3 max |  |  |
| Steering wheel (cracks/color) | 3 |  |  |
| Convertible top (3 piece rear window) Top, snaps, 4 Philips head screws | 6 |  |  |
| Top boot (condition) | 3 |  |  |
| Wrong color (top & boot) (tan for code P-903, tan or black for P904/6, black all other colors) | (5)* |  |  |
| Top irons (color- gloss black/condition) | 3 |  |  |
| Trunk area - w/external lid (interior of trunk body color/condition) (wiring, rubber trunk mat) | 5 |  |  |
| If No rubber trunk floor mat after E59048 | (1)* |  |  |
| Jack/handle & instructions (jack should be black) check for stripped threads on nut (instructions on heavy card stock with hole reinforcements and cotton string) | 3 |  |  |
| Total deductions ______ Judge__________________________________________________ *NUMBERS IN PARENTHESES ARE AUTOMATIC DEDUCTIONS page 5 |
| METROPOLITAN JUDGING FORM |
| CAR# CONCOURS CLASS |
| FEATURE | MAX DED | DED | COMMENTS |
| ENGINE |
| Air conditioning/cruise control/power steering added (3)* each | (3)* |  |  |
| Engine compartment paint (body color/condition) | 5 |  |  |
| Hood bumpers & cowl lacing/clips (Check for correct clips, missing hood bumpers) | 6 |  |  |
| Data plates (condition/missing) Deduct for incorrect fasteners, missing paint, engraved plates, bent or missing plates. | 10 |  |  |
| Hood safety catch (plating/condition) Deduct for missing, cracked/broken, or welded latches. Incorrect plating, broken spring, missing strap. | 3 |  |  |
| Fan belt (fabric) | 2 |  |  |
|  | Notched fan belt | (1)* |  |  |
| Engine block (Green or Red for prefix 1G, 2G, Green beginning E11001, 1500 series IH/15CNH/15ANH/15FNH beg. E21008 (bent dip stick after E74192) | 8 |  |  |
| Wrong Engine (Non Met Engine) Incorrect Met motor, deduct 5 points per generation A’ Series 1200 to E-11003 with water pump bypass hose. B’ Series 1200 to E-21007 without bypass hose. 1st Series 1500 to E-43115 with no oil filter. 2nd Series 1500 to end of production w/oil filter. | (40)* 15 |  |  |
| Intake/exhaust manifold. (vacuum fitting on intake beg. E27986) (engine color) check for gas line overflow tube. | 4 |  |  |
| Bonus Spark plugs if AG-5, N-8, N16Y, or UN12Y | 2 |  |  |
| Ignition (spark plug) wires | 4 |  |  |
| Oil filter (partial flow avail. Beg.E21008, full flow avail. Beg.E45245) | 1 |  |  |
|  | Screw on oil filter adaptor | (2)* |  |  |
| Carburetor (C–1386/1466, C-1528M/1630 beg. E21008) Deduct for incorrect part number carburetor and incorrect dated carburetor | 5 |  |  |
| Air cleaner (black) (change beg. E21008) Deduct for wrong air cleaner, dry filter air cleaner assemblies, dents, rust and incorrect braces. | 5 |  |  |
| Vacuum line (condition) Deduct for missing support, missing line | 1 |  |  |
| Coil (screw top, aluminum Body, decal and looped mounting base.) | 3 |  |  |
| Page #6 |

| METROPOLITAN JUDGING FORM |
| --- |
| CAR# CONCOURS CLASS |
| FEATURE | MAX DED | DED | COMMENTS |
| ENGINE |
| Distributor (40284H, 40438 beginning E11001, 40427/ 40499/ 40600A beg. E21008, 40600H beg. E59643) Deduct for incorrect distributor part number, incorrect date for engine build, no paint, no Lucas on distributor cap and missing plug wire holder.) | 3 |  |  |
| Fan (red or yellow) four blades began E-11001 | 2 |  |  |
| Fuel supply (braded hose to fuel pump, no inline filter) | 2 |  |  |
|  | No primer rod on fuel pump | (1)* |  |  |
|  | Electric fuel pump | (10)* |  |  |
| Generator (22258, beg. E21008 22700B) (engine color) | 2 |  |  |
| Head/valve cover (engine color, oil filler moves to front E11001) | 5 |  |  |
| Heater (black) (condition/data plates) | 5 |  |  |
| Hoses Upper/Lower Radiator hoses, T-hose, and metal pipes. (no drain hoses from cowl vent) | 5 |  |  |
|  | Drain hoses from cowl vent housing | (1)* |  |  |
| Clamps (wire type) | 8 |  |  |
| Radiator cap, (4 lb.) | 2 |  |  |
| Bonus AC- 4 lb. Cap | 1 |  |  |
| Radiator core (finned/black) (condition) Deduct for wrong color and missing tags | 4 |  |  |
| Starter (engine color) Starter Switch Deduct for incorrect number, date, frayed cables, torn/missing boots and plastic base switch | 6 |  |  |
| Wiring (tape wrapped/condition) (courtesy light avail. Beg. E21008) Deduct for “Crimp Type” connectors, exposed connectors, and incorrect wires. | 6 |  |  |
| Voltage regulator Deduct for voltage regulators without Lucas covers and/or missing fuses | 2 |  |  |
| Water pump (engine color) Deduct for incorrect pulleys and/or unpainted water pumps | 2 |  |  |
| Other (Overall cleanliness from new car prep) |  |  |  |
| Total deductions _______ Judge_____________________________________________________ *NUMBERS IN PARENTHESES ARE AUTOMATIC DEDUCTIONS page 7 |

| METROPOLITAN JUDGING FORM |
| --- |
| JUDGING SUMMARY |
| CAR # | YEAR |
| OWNER (S) |
| TOTALS |
| EXTERIOR |  |  |
| CHASSIS |  |  |
| INTERIOR |  |  |
| ENGINE |  |  |
| TOTAL DEDUCTIONS |  |  |
| 400 --- _______ total deductions |
| POINTS AWARDED 400- TOTAL DEDUCTIONS |
| 400 – 375 GOLD 374 – 350 SILVER 349 – 325 BRONZE AWARD EARNED _______________________________________ Chief Judge___________________________________________ |